## Slide 1: Flow control and error control techniques in the data link layer protocols
Group members:
1.Joy Bhowmick ID:2015-2-60-061
2.Sazzad Hossen ID:2015-2-60-057
3.Anik Kumar Das ID:2015-2-60-040

## Slide 2: Contents
Introduction
What is CRC-16
Why we used CRC-16
How it works
Go Back n protocols
How it works
Applications of CRC-16

## Slide 3: Introduction
A cyclic redundancy check (CRC) is an error-detecting code commonly used in digital networks and storage devices to detect accidental changes to raw data. Blocks of data entering these systems get a short check value attached, based on the remainder of a polynomial division of their contents. Go-Back-N ARQ is a specific instance of the automatic repeat request (ARQ) protocol, in which the sending process continues to send a number of frames specified by a window size even without receiving an acknowledgement (ACK) packet from the receiver. It can transmit N frames to the peer before requiring an ACK.

## Slide 4: How CRC-16 works
It is a 16 bit string which is used for computing checksum of any given data. It is used like an error detecting devices. If the remainder of the raw data is all zeros(0) then the data is error free and if not then there was an error in the given data.

## Slide 5: Go Back n protocols
Go-Back-N ARQ is a specific instance of the automatic repeat request (ARQ) protocol, in which the sending process continues to send a number of frames specified by a window size even without receiving an acknowledgement (ACK) packet from the receiver. It can transmit N frames to the peer before requiring an ACK. It can be better performed than stop and wait protocols.

## Slide 6: How it works
The receiver process keeps track of the sequence number of the next frame it expects to receive, and sends that number with every ACK it sends. The receiver will discard any frame that does not have the exact sequence number it expects and will resend an ACK for the last correct in-order frame.

## Slide 7: Conclusion
Go Back n protocols performs better than stop and wait protocols but there are some problem in this protocol. If any frame is lost then we go to that frame and the next sequence number will discarded automatically. The best solution of this problem is selective reject protocols.